## Slide 1: Refraction Seismology
Snell’s Revenge!
Christiaan Huygens
(1629-1695)
Wavelets
Rule!
Burger, Sheehan, Jones: Chapters 2.2, 3.1, 3.2, 3.3

## Slide 2: Our Geophysics Toolbox
Selecting the right geophysics tool depends on our target:
  How deep? How big? What physical properties do we need to know? What do we already know? What is the resolution needed to solve our engineering/environmental/hazard problem?

## Slide 3
Layer thickness, layer velocity
Horizontal boundaries
Layer thickness, velocity, contrast
Horiz boundaries, lateral transitions
3-D seismic velocity
boundaries of many orientations
earthquake mechanics

## Slide 4: Resolution
Choosing the right tool—what do we need to resolve?
For seismology—vertical resolution is 0.25*wavelength
(wavelength=velocity/frequency)
Average P-wave crustal velocity: ~6000 m/s or 6 km/s
Frequencies: Earthquakes very broad range
- for 10 Hz waves, wavelength = 600 m
- for 1 Hz waves, about 6 km
Airguns: 3-900 Hz
Resolution chart for camera testing

## Slide 6: Finding Ray Paths :: Refraction
Just like light, seismic rays refract, or bend, when they encounter a medium of different seismic velocity
Refraction is quantified by Snell’s Law
  = angle of incidence
    Measured from normal to interface
  = seismic velocity of material
At some value where i > ic , the wave is completely reflected
i1
i2
v1
v2
v1 < v2
An orangutan spear fishing
Curse you
Snell’s law!!

## Slide 7: Fermat’s Principle
If velocity is NOT uniform:
  The path of least time is a not a straight line
  The wave must bend or refract at the interface
Pierre de Fermat (1601-1665): A French lawyer and amateur mathematician.
Fermat’s Principle: Light (and any wave, in general) travels in the path that takes the least amount of time between two points.
If velocity is uniform:
  The path of least time is a straight line
A
B
A
B
V1
V2
*Assuming V1 > V2

## Slide 8: Snell’s Law & Critical Refraction
Seismic sources radiate waves in all directions
Some ray must hit interface at exactly the critical angle, ic
This critically oriented ray will then travel along the interface between the two layers
If more oblique than critical, all wave energy is reflected
  The reflected energy is useful too! And we’ll see it over the next couple weeks

## Slide 9: Refraction, Velocity and Arrival Times = Moho Discovery
Seismic waves travel faster through the mantle than the crust
In 1909, Andrija Mohorovičić discovered that waves first arriving at seismic stations within 200 km of an epicenter had an average velocity of 6 km/s
Stations > 200 km away
average wave speed 8 km/s
To explain this
nearby stations received waves that only went through the crust
far away stations received waves that travel through the mantle.
The crust mantle boundary is now called the Moho, in honor of this discovery

## Slide 10: Potential Paths in a Refraction Survey
When doing a seismic refraction survey, a recorded ray can come from three main paths
  The direct ray
  The reflected ray
  The refracted ray
Because these rays travel different distances and at different speeds, they arrive at different times
The direct ray and the refracted ray arrive in different order depending on distance from source and the velocity structure
Direct Ray
ic
ic
Reflected Ray
Refracted Ray
Shot Point (i.e. the Source)
Receiver
v1
v2
Layer 1
Layer 2
Why are these rays straight lines?

## Slide 11: The Time-Distance (t-x) Diagram
Think about:
What would a fast velocity look like on this plot?
Why is direct ray a straight line?
Why must the direct ray plot start at the origin (0,0)?
Why is refracted ray straight line?
Why does refracted ray not start at origin?
Why does reflected ray start at origin?
Why is reflected ray asymptotic with direct ray?
Understanding The t-x Diagram is Key!!!

## Slide 12: The Direct Ray
The Direct Ray Arrival Time:
  Simply a linear function of the seismic velocity and the shot point to receiver distance
Direct Ray
Shot Point
Receiver
v1
v2
Layer 1
Layer 2
Time (t)
Distance (x)

## Slide 13: The Reflected Ray
The Reflected Ray Arrival Time:
  is never a first arrival
  Plots as a curved path on t-x diagram
  Asymptotic with direct ray
  Y-intercept (time) gives thickness
    Why do we not use this to estimate layer thickness?
Shot Point
Receiver
v1
v2
Layer 1
Layer 2
Time (t)
Distance (x)
Y-intercept

## Slide 14: The Refracted Ray
The Refracted Ray Arrival Time:
  Plots as a linear path on t-x diagram
    Part travels in upper layer (constant)
    Part travels in lower layer (function of x)
  Only arrives after critical distance
  Is first arrival only after crossover distance
    Travels long enough in the faster layer
ic
ic
v1
v2
Layer 1
Layer 2
ic
“Critical Distance”
No Refracted Rays 
ic
critical
distance
crossover
distance
Time (t)
Distance (x)

## Slide 15: Making a t-x Diagram
v1 = 1/slope
v2 = 1/slope
Y-intercept to find thickness, h1
or
Refracted Ray Arrival Time, t

## Slide 17: Multiple Layers
Seismic refraction can detect multiple layers
The velocities are easily found from the slopes on the t-x diagram

## Slide 18: Refraction…What is it Good For?
Seismic refraction surveys reveal two main pieces of information
  Velocity structure
    Used to infer rock type
  Depth to interface
    Lithology change
    Water table

## Slide 19
Applications – saturated rock, depth to bedrock, degree of weathering

## Slide 20
Applications – Geotechnical/engineering
Rippability measures the degree of difficulty to excavate any given soil or rock
It is a significant aspect of the preliminary work of any civil engineering project

## Slide 21: Socorro Data using SeisImager2D
Ian Podmore

## Slide 22: Picking 1st Arrivals
Process was done in SeisImager’s Pickwin software
Set geophone offset and shot location manually
Pick first arrival for each geophone, then repeat process for all 24 shot gathers
Raw data looks better than stacked waveforms in most cases

## Slide 23: Travel Time Curves
Once all shots have 1st arrivals picked, import data to Plotrefa software
Plotrefa offers 2 options: 2-layer model and 3-layer model
We also tricked it into a 1-layer model
1 layer interpretation

## Slide 24: Travel Time Curves
Once all shots have 1st arrivals picked, import data to Plotrefa software
Plotrefa offers 2 options: 2-layer model and 3-layer model
We also tricked it into a 1-layer model
2 layer interpretation

## Slide 25: Travel Time Curves
Once all shots have 1st arrivals picked, import data to Plotrefa software
Plotrefa offers 2 options: 2-layer model and 3-layer model
We also tricked it into a 1-layer model
3 layer interpretation

## Slide 26
1 layer inversion

## Slide 27
2 layer inversion

## Slide 28
3 layer inversion